## Slide 1: Multivariable System Poles
MIMO: Poles are collection of all poles of individual transfer function.
Example:
The transfer function matrix has single poles at
A MIMO system is stable if all the poles of the transfer function matrix lie in the left-half plane (LHP); otherwise it is unstable.
The poles of a transfer function matrix, and the eigenvalues of the equivalent system matrix A in the state-space form, are one and the same
The poles of the multivariable system are the roots of:
| (sI - A) |= 0

## Slide 2: Multivariable System Zeros
The roots of the equation:
MIMO: poles of the inverse of the transfer function matrix G(s)
are the zeros of the transfer function matrix G(s).
Poles and zeros may be in the same location. Must ensure that there has been no pole-zero cancellation when forming the determinant.

## Slide 3: Controllability
Controllable: if the controlled variables can be maintained at their set points, in steady state, in spite of disturbances entering system.
Assume system begins at a steady state, the system is controllable
Controlled variables can be maintained at set points, by adjusting the specified MVs in step like disturbances.
The steady state can be determined by the final value theorem.
State space model
A solution exists for a square system of linear equations when an inverse to the matrix of feedback process gains (K) exists; thus, the system is controllable if the determinant of the gain matrix is nonzero.

## Slide 4: Stability
BIBO stability: A MIMO process is stable if and only if all the poles of the transfer function matrix have negative real parts; otherwise it is unstable.
In relation to the equivalent state-space form, the multivariable system poles resulting from evaluating the determinant:
Stability requires the roots of the equation all lie in the LHP. It is identical for stabilty in terms of its transfer function matrix or its state-space model.

## Slide 5: Singularity — Singular Values
Matrix is singular: determinant is zero,
The measure of the near singularity of a matrix can be found from the singular values of the matrix, defined as
Condition number: The ratio of the largest and smallest singular value
The condition number provides a reliable indication of the onset of singularity, or “ill-conditioning.”
where A* is the transpose of the complex conjugate and λi(A*A) represents the ith eigenvalue of the matrix (A*A)