## Slide 1: Steady State RGA
To relax restrictions, consider steady state
with:
First-principles method
Matrix operation
K : steady-state gain matrix of G(s)
R: transpose of the inverse of K:

## Slide 2: Interpretation of the RGA
Gain amplification - loop gain increased if other loops are closed
Look at both sign and magnitude
Gain reversal occurs when other loops are closed - undesirable
Open loop gain is zero, control action depends on other control loops being closed – not select
  instability due to incorrect controller action
Loss of control when other loops are closed - gain goes to zero
  undesirable
No interaction: open-loop gain unaffected by other loops
  desirable - one-way interaction still possible
Attenuation of open-loop gain when other loops are closed

## Slide 3: The Niederlinski Criterion
Test instability based on steady-state information
Arrange transfer function matrix: pairings are on diagonal
Stable - process elements must be open-loop stable
Proper - order of denominator greater than order of numerator
Individual control loops are closed-loop stable
Closed-loop unstable, if
Sufficient condition: if condition not satisfied, no instability detected --> this does NOT imply stability
use as a screening tool - identify problem cases

## Slide 4
RGA and NI Based Pairing rules
Loop pairing Rules
RGA and NI based loop pairing rules requires that manipulated and controlled variables be paired:
Corresponding RGA elements are closest to 1.0.
Corresponding RGA elements are positive.
The NI is positive.
Large RGA elements should be avoided.

## Slide 5: Normalized Gain
Define normalized gain

## Slide 6: Relative Normalized Gain Array
RNGA

## Slide 7: Loop Pairing Based on RNGA
RNGA and NI based loop pairing rules requires that manipulated and controlled variables be paired:
Corresponding RNGA elements are closest to 1.0.
Corresponding RGA elements are positive.
The NI is positive.
All paired RNGA elements are positive.
Large RNGA elements should be avoided.

## Slide 8: Forms of Controls
Decentralized control:
Sparse Control:
Centralized control:

## Slide 9: Normalized Interaction Index
Put paired loops in diagonal position, define
Relative control performance index (RCPI),
= 0: centralized;  = 1: decentralized controller
0<<1, smaller , better overall control system performance achievable, block diagonal controller or sparse controller would be preferred
if all off-diagonal elements less than 0.15, decentralized control can result in satisfactory performances.
If some off-diagonal elements close to 1, block diagonal controller or sparse controller would be preferred

## Slide 10: Relative Average Residence Time
Define relative average residence time (RART)
By RNG
then
Since
RART

## Slide 11: ETF Based on RNGA Approximation
Assigning the Equivalent Transfer Function (ETF) when other loops are closed to have the same structures as the open-loop transfer functions,
ETFs when the control system is closed can be approximated as:
By relative gains and relative average resident times

## Slide 12
Closed Loop ETF
By assuming perfect control and matrix calculation
Compare the Two, Important Relation